## Slide 1
Installation Instructions
Windows 8 http://mytechblog.com/tutorials/arduino/install-arduino-drivers-on-windows-8/
Windows 7, Vista, and XP
https://www.arduino.cc/en/Guide/Windows#toc4

## Slide 2
Plug in your board and wait for Windows to begin it's driver installation process. After a few moments, the process will fail, despite its best efforts
Click on the Start Menu, and open up the Control Panel.
While in the Control Panel, navigate to System and Security. Next, click on System. Once the System window is up, open the Device Manager.
Look under Ports (COM & LPT). You should see an open port named "Arduino UNO (COMxx)". If there is no COM & LPT section, look under "Other Devices" for "Unknown Device".
Right click on the "Arduino UNO (COmxx)" port and choose the "Update Driver Software" option.
Next, choose the "Browse my computer for Driver software" option.
Finally, navigate to and select the driver file named "arduino.inf", located in the "Drivers" folder of the Arduino Software download (not the "FTDI USB Drivers" sub-directory). If you are using an old version of the IDE (1.0.3 or older), choose the Uno driver file named "Arduino UNO.inf"
Windows will finish up the driver installation from there.

## Slide 3
To do this, open the charms bar and click Change PC Settings. Then go to General and under Advanced Startup and click Restart Now.
When the computer starts up click Troubleshoot
Then Advanced Options
From the next menu select Startup Settings and then Restart
The screen displayed allows you to “Disable driver signature enforcement” by pressing key 7.
Wait for the computer to restart and follow through the Arduino’s instructions again. You will be presented with a security warning when installing the drivers.
Click Install this driver software anyway and the installation will continue.

## Slide 5
To do this, open the charms bar and click Change PC Settings. Then go to General and under Advanced Startup and click Restart Now.

## Slide 6
When the computer starts up click Troubleshoot

## Slide 7
Then Advanced Options

## Slide 8
From the next menu select Startup Settings and then Restart

## Slide 9
The screen displayed allows you to
“Disable driver signature enforcement” by pressing key 7.

## Slide 10
Wait for the computer to restart and follow through the Arduino’s instructions again.
You will be presented with a security warning when installing the drivers.
Click Install this driver software anyway and the installation will continue.

## Slide 11: Interactive Posters Capacitive Sensing with Arduino

## Slide 12: What does Codasign do?

## Slide 14: What is an Arduino?

## Slide 15: Description of Arduino
Arduino is an open-source electronics prototyping platform based on flexible, easy-to-use hardware and software. It's intended for artists, designers,
hobbyists, and anyone interested in creating interactive objects or environments.

## Slide 16: Arduino diagram8

## Slide 17: Description of Arduino
Arduino Programming Environment
The Arduino software is also open-source. The source code for the Java environment is released under the GPL and the C/C++ microcontroller libraries are under the LGPL.

## Slide 18: Breadboard Layout

## Slide 19: Light Emiting Diode
Notes: Ground – cathode = cat like to lie on the ground
*

## Slide 20: Resistor
They reduce the current that flows across them and are
useful for making sure other components aren't overloaded
with too much current.

## Slide 21: Potentiometer & LED Fade

## Slide 25: Photo Resistor & LED

## Slide 29: Capacitive & LED

## Slide 30
connects to your
tin foil

## Slide 33
Pin 4
Send pin
Pin 2
Receive pin
1. SEND pin moved to a new state
2. waits for the RECEIVE pin to change
3. reports the variable's value
which is in arbitrary units.

## Slide 34: Capacitive & Piezo

## Slide 36: END
www.codasign.com
Info@codasign.com
@codasign

## Slide 37: END
http://arduino.cc/en/Guide/UnoDriversWindowsXP
http://arduino.cc/en/Guide/windows
Windows install guide
Windows step by step